## Slide 1: TremorTrack – Low-Cost Parkinson’s Disease Hand Tremor Monitoring System
Team name :
Lochan
Team members:
Lochan Reddy R 1BI24EC069
Manya V 1BI24EC076
Nisarga R 1BI24EC090
Dept of electronics and communication

## Slide 2
Problem Statement:
Monitoring hand tremors in Parkinson's Disease (PD) patients is currently subjective, intermittent, and clinic-dependent. Tremor severity fluctuates heavily throughout the day based on fatigue, stress, and medication cycles ("On/Off" periods). Because evaluation only happens during periodic hospital visits, there is a critical lack of affordable, real-time tracking solutions outside the hospital. This makes it highly difficult to track long-term disease progression and optimize daily pharmaceutical dosages accurately.
Objective:
To build an affordable, standalone engineering solution that shifts objective Parkinsonian symptom monitoring from the clinic straight to the patient's home environment.

## Slide 3
Removing Subjectivity:
Replaces vague descriptions ("my hand feels shakier today") with an empirical, quantifiable scale (0–10) that gives both the patient and doctor a precise baseline.
Tracking Medication Efficacy:
Helps patients accurately log how well their medication is managing their tremors throughout the day, removing the anxiety of guesswork.
Early Deterioration Warning:
Consistent upward trends in daily home data can flag rapid progression or medication tolerance issues early, allowing for timely medical interventions before a severe motor crisis occurs.
CUSTOMER PAIN POINT ADDRESSED

## Slide 4
Objective-to-Digital Mapping:
Translates physical, multidimensional Parkinsonian motor symptoms directly into a clear digital score (0–10) in real time.
Integrated Standalone Tracking:
Features native on-board memory routines to store, access, and cross-reference a patient's historical tremor data completely offline.
Automated Trend Evaluation:
The firmware automatically compares the current session against a saved baseline to instantly output a progressive trend direction (Increasing / Decreasing / No Change).
BRIEF ABOUT THE INNOVATIVENESS

## Slide 5: FEASIBILITY
Technical Feasibility:
Utilizes responsive microcontrollers and high-precision I2C communication protocols capable of handling micro-motion acceleration variables seamlessly with near-zero computation latency.
Economic Feasibility:
Built completely using widely available consumer electronics components, reducing the bill of materials significantly compared to expensive clinical diagnostics. This bridges the economic gap for low-income populations.

## Slide 6: PROBLEM SOLUTION
The System:
A compact, portable device that intercepts physical hand tremors via an inertial measurement unit, processes the frequency fluctuations over a set timeline, and prints out a definitive assessment.
User Control Interface (Single Button):
Short Press: Toggles measurement loops on or off. Upon stopping, the value is saved as the baseline.
Long Press (2 Seconds): Instantly flushes the system cache, resetting all previous data points.
Dynamic Information Output (LCD Screen) And the remote diagnosis:
Displays current tremor level, saved baseline value, current trend direction, and an explicit clinical status classification (Stable / Moderate / Severe) and also displays the trends on a webpage.

## Slide 7: COMMERCIAL VIABILITY
Target Audience:
An aging global population where Parkinson’s Disease and related neurodegenerative motor disorders are growing rapidly.
Market Position:
Positioned as an essential, hyper-affordable everyday home monitoring utility. It acts as a continuous data-bridge between periodic neurological consultations.

## Slide 8: TECHNOLOGY USED
Core Domains:
Embedded Engineering, Real-Time Signal Processing, Inertial Measurement.
System Hardware Stack:
Microcontroller: ESP32 (Handles dual-core data computation and logic profiling).
Sensor Unit:
MPU6050 (High-accuracy integrated 3-axis accelerometer and gyroscope to track rapid physical shaking).
Display Unit: 16x2 LCD Display for a high-contrast, patient-friendly UI.
Input Switch:
Robust tactile push-button designed for easy use by individuals experiencing motor control issues.

## Slide 9: .
The Companion App (Mobile Gateway)
Heading: Patient Companion
Bullet Points:
Pairs via Bluetooth to fetch local scores from the hardware.
Acts as a localized digital diary for the patient.
Syncs data automatically to a secure cloud database.

## Slide 10: RESEARCH CARRIED OUT
Symptom Frequency Analysis:
Researched the distinct frequency profiles of Parkinson's rest tremors (typically resting between 4–6 Hz) to distinguish them from standard physiological hand movements or noise.
Algorithmic Modeling:
Evaluated mathematical variance calculations required to map raw, volatile spatial acceleration vector streams (x, y, z) into stable, intuitive 0–10 integers.

## Slide 11: PROTOTYPE/ POC DEVELOPED
Demo Functional Workflow:
System boots into a low-power, idle state.
Patient clicks the tracking button MPU6050 begins logging continuous spatial movement data.
Processing loops calculate variance thresholds (higher mechanical fluctuations output a higher numerical score).
Second press stops the routine, locks the value in memory as a baseline, and automatically runs comparative matches against future cycles to display the directional disease trend.
The same is also displayed on an online webpage for remote clinical diagnosis.

## Slide 12: SCOPE FOR PATENTABILITY
Novel Utility Framework:
The patentability or utility scope focuses not on complex mathematical filtering, but on the specific hardware-firmware workflow that turns an ultra-low-cost, standard motion sensor into a standalone comparative monitoring system integrating hardware and software via a webpage.
Local Delta-Tracking Logic:
The novelty lies in the lightweight code layout that allows a basic microcontroller to:
Capture a real-time data session.
Cache that specific session value as a local baseline.
Run an automatic mathematical comparison (current reading minus saved baseline) to instantly output a progressive trend direction (Increasing / Decreasing / Stable) directly on an affordable 16x2 LCD display.
Displays this on a remote online platform for clinical evaluation.
Low-Cost Accessibility Design:
Packaging this entire tracking and comparison loop into a single-button user interface designed specifically for Parkinson's home care utility.

## Slide 13: FUTURE PLANS
Clinical Data Telemetry:
Adding integrated Wi-Fi or Bluetooth protocols to auto-sync daily home monitoring data directly with secure medical cloud records for remote hospital access.
Form Factor Optimization:
Redesigning the desktop prototype layout onto a custom micro-PCB and integrating it into an ergonomic, wearable wristband or a specialized diagnostic tracking glove.

## Slide 14: ADD SCREENSHOT OF RESULTS

## Slide 15: DEMONSTRATION VIDEO